# Repository Information
1. Name
  1. modular_device_base_3x2
2. Version
  1. 1.2
3. License
  1. Open-Source Hardware
4. URL
  1. https://github.com/janelia-kicad/modular_device_base_3x2
5. Author
  1. Peter Polidoro
6. Email
  1. peterpolidoro@gmail.com
## Description
This board is the base of 3x2 format modular devices. It is a breakout board for the microprocessor, with connections for power, communication, and top boards.
# Images

# Schematic
./schematic/modular_device_base_3x2.pdf

# Gerbers
Save gerbers zip file and send to your favorite PCB manufacturer for fabrication.
./gerbers/modular_device_base_3x2_v1.2.zip

# Bill of Materials
## PCB Parts
Item	Reference(s)	Quantity	PartNumber	Vendor	Description
1	C1 C2 C3 C4 C5	5	445-4536-1-ND	digikey	CAP CER 10UF 50V 10% X7S 1210
2	C6	1	399-13229-1-ND	digikey	CAP CER 0.1UF 100V X7R 1210
3	D1 D2	2	LSM115JE3/TR13CT-ND	digikey	DIODE SCHOTTKY 15V 1A DO214BA
4	D3 D4 D5 D6 D7 D8 D9	7	568-11697-1-ND	digikey	DIODE SCHOTTKY 45V 10A CFP15
5	L1	1	350-1712-ND	digikey	LED 2MM 5V RT ANGLE RED PCMNT
6	L2	1	350-1717-ND	digikey	LED 2MM 5V RT ANGLE GREEN PCMNT
7	L3	1	350-1719-ND	digikey	LED 2MM 5V RT ANGLE YELLOW PCMNT
8	MDB1	2	S7049-ND	digikey	16 Position Header Through Hole Female Socket
9	MH1 MH2 MH3 MH4	4	36-2027-ND	digikey	Round Standoff Threaded 4-40 Aluminum 0.500in 0.187in
10	P1	1	CP-063BH-ND	digikey	CONN PWR JACK DC 2.5X5.5 8A T/H
11	P2	1	ACX1655-ND	digikey	CONN BNC JACK R/A 75 OHM PCB
12	P3 P5	2	A100890CT-ND	digikey	CONN HEADER 3POS R/A SMD GOLD
13	P4 P6	2	A100903CT-ND	digikey	CONN HEADER 2POS R/A SMD GOLD
14	P7	1	732-5336-ND	digikey	CONN HEADER 3 POS RA 2.54
15	P8	1	SAM10781-ND	digikey	CONN HEADER 2POS .100in SNGL SMD
16	R1	1	P6.19KAACT-ND	digikey	RES SMD 6.19K OHM 1% 1/2W 1210
17	REG1	1	945-1395-5-ND	digikey	CONV DC/DC 1A 5V OUT SIP VERT
18	SW1	1	CKN1860CT-ND	digikey	SWITCH TACTILE SPST-NO 1VA 32V
19	TEENSY1	1	1568-1231-ND	digikey	DEV TEENSY 3.2 13736
20	U1	1	MAX6817EUT+TCT-ND	digikey	IC DEBOUNCER SWITCH DUAL SOT23-6

## Supplemental Parts
Item	Quantity	PartNumber	Vendor	Description
1	1	EPS594-ND	digikey	30 WATT DESKTOP POWER SUPPLY 24V
2	1	993-1037-ND	digikey	CORD 3COND NEMA PLUG 320-C5
3	1	A106625CT-ND	digikey	14 Positions Header Unshrouded Breakaway Connector 0.100in 2 row SMD
4	2	S1011EC-24-ND	digikey	24 Positions Header Unshrouded Breakaway Connector 0.100in 1 row Through
5	1	S9001-ND	digikey	CONN JUMPER SHORTING GOLD FLASH
6	1	AE10342-ND	digikey	CABLE USB-A TO MICRO USB-B 2M

## Vendor Parts Lists
./bom/digikey_parts.csv
./bom/supplemental_digikey_parts.csv